## Slide 1: CCTV Risk Intelligence Stack
Hackathon prototype — multimodal perception, fused risk scoring, RL escalation, RAG ops briefs
Stack: Python · Ultralytics YOLOv8 · OpenCV · PyTorch · Streamlit · LangChain · FAISS · scikit-learn · Gymnasium

## Slide 2: Objective & Problem Framing
Goal: operator-assist screening from fixed CCTV — not identity recognition.
Gap: raw detections are insufficient; need temporal context, fusion, and actionable escalation hints.
Deliverable: end-to-end pipeline — video ingest → CV features → normalized risk vector → policy hint → UI + logs.
Scope: demo / research — not certified for legal adjudication or automated enforcement.

## Slide 3: End-to-End Pipeline (Data Flow)
Ingest: MP4/AVI/MOV/MKV via Streamlit or CLI (OpenCV VideoCapture).
Per-frame: YOLOv8 inference (Ultralytics) + classical CV (Farneback optical flow on person ROI mask).
Tracking proxy: centroid-based SimpleBagTracker → abandoned-object dwell estimate (seconds).
Fusion: compute_risk() — weighted linear combination of L1-normalized component scores → scalar 0–100.
Policy: tabular Q-learning state from discretized risk + action cooldown → discrete escalation action ID.
Presentation: annotated frames (OpenCV overlay) + Plotly time-series + optional RAG operator brief.

## Slide 4: Perception Layer (Computer Vision)
Detector: YOLOv8n (default) or custom .pt; class-to-head mapping via model.names at runtime.
Buckets: person / baggage (COCO) · weapon proxies (COCO bat/racket + user-defined) · fight/theft/accident (custom class sets + heuristics) · missile/drone (custom-only).
Motion: cv2.calcOpticalFlowFarneback on grayscale; robust normalization (p95 magnitude) → motion_score ∈ [0,1].
Crowding: pairwise centroid distance graph on person boxes → proximity_cluster_score.
Road context: COCO vehicle classes + spatial proximity heuristic → accident_like (demo; train crash class for production).
Output per frame: FrameSignals dataclass — boxes, tags, scalar cues for downstream fusion.

## Slide 5: Risk Fusion & Semantic Labels
Architecture: transparent weighted sum — Σ weight_i × component_i × 100; weights sum to 1.0 in risk_scorer.WEIGHTS.
Components (excerpt): crowd_density, motion_anomaly, abandoned_object, acoustic_threat, weapon_like, missile_like, drone_like, wifi_rf_anomaly, fight_like, theft_like, accident_like.
Thresholded tags: e.g. disturbance_motion, unattended_object, fight_like_unverified, road_accident_hint_unverified.
RL state: risk_bucket(score) maps continuous score to discrete 0..9 for Q-table indexing.
Logging: per-frame dict → pandas DataFrame → CSV / in-UI charts (area stack of normalized components).

## Slide 6: Auxiliary ML & Retrieval Modules
RL: Gymnasium-compatible tabular Q-learning; Q-table persisted as models/q_table.npy; ε-greedy-style exploration during offline train_q_table().
RAG: LangChain + Chroma/FAISS vector store over chunked playbook text; sentence-transformers embeddings; retrieve_context() + rag_operator_brief() for NL operator summaries.
Wi-Fi / RF cue: Isolation Forest on ISOT-style flow feature vectors; optional embedding-distance blend; scalar wifi_rf_anomaly_score fused into video risk.
Audio: short-time energy / transient heuristic (waveform) → acoustic_threat channel (demo, not gunshot classifier).

## Slide 7: Application & Integration Layer
UI: Streamlit multi-tab app — video analysis, help/geo notify, RAG console, Wi-Fi workflow, audio upload.
Video I/O: browser-safe encoding via open_video_writer() — tries avc1/H264/X264/mp4v then MJPG AVI fallback.
Viz: Plotly Express / Graph Objects for risk vs time and stacked component areas.
Alerts: notify_operator() + format_alert_location() — simulates dispatch with optional fixed camera lat/lng.
Batch path: process_video.py — same analyzer + fusion; exports annotated video + events.csv.

## Slide 8: Limitations, Ethics & Next Steps
Accuracy: default weights are COCO-biased; fight/accident/weapon require domain-specific YOLO fine-tuning (Ultralytics train; YAML dataset; class-name parity with UI).
Heuristics: high false-positive rate on busy roads; always human-in-the-loop review.
Privacy: design targets scene-level risk — avoid PII linkage; comply with local surveillance law.
Engineering: edge ONNX/TensorRT export, multi-camera fusion, calibrated thresholds, SOC2-style audit logs.
Q&A — thank you.